Pinouts - CPU - Signal Summary

Advance Gameboy CPU Signal Summary
Cart Bus: D0-D7, A0-A15, /CS, /RD, /WR (different usage in GBA/DMG mode)
WRAM Bus: WA0-WA16, WD0-WD15, /WLB, /WUB, /WWE, /WOE (used in GBA mode only)
LCD Bus : LDR1-5, LDG1-5, LDB1-5, DCK, LP, PS, SPL, CLS, SPS, MOD, REVC
Joypad: TP0-3 (Buttons), TP4-7 (Directions), TP8-9 (L/R-Buttons, via R43/R44)
Serial Link: SC, SD (aka P14?), SI, SO - Audio: SO1-2, Vin
Other: CK1-2, PHI, IN35, VCNT5, /FIQ (via CL1 to VDD3), /RESET (IN), /RES (OUT)
Supply: VDD35, VDD3, VDD2, GND (some are probably undoc inputs)
GBA SP: Same as GBA, plus VDD1, plus duplicated supply pins, plus pin 152.
Pinouts - CPU - Pinouts

Advance Gameboy CPU Pinouts (CPU AGB)
1 VDD3 17 D0 33 A0 49 WA4 65 VDD2 81 WD9 97 LDB5 113 CK1 / 2 IN35 18 A15 34 /CS 50 WA5 66 WD5 82 WD1 98 LDB4 114 CK2 / 3 TP8 19 A14 35 /RD 51 WA6 67 WD13 83 /WOE 99 LDB3 115 VDD2 / 4 TP0 20 A13 36 /WR 52 WA7 68 WD6 84 DCK 100 LDB2 116 GND / 5 TP1 21 A12 37 PHI 53 /WLB 69 WD14 85 LP 101 LDB1 117 VDD2 / 6 SO1 22 A11 38 VDD35 54 /WUB 70 WD7 86 PS 102 GND 118 VCNT5 / 7 SO2 23 A10 39 GND 55 /WWE 71 WD15 87 LDR5 103 VDD3 119 TP9 / 8 Vin 24 A9 40 SC 56 WA8 72 WD8 88 LDR4 104 SPL 120 TP6 / 9 /RES 25 A8 41 SD 57 WA9 73 WD16 89 LDR3 105 CLS 121 TP5 / 10 D7 26 A7 42 SI 58 WA10 74 WA16 90 LDR2 106 SPS 122 TP7 / 11 D6 27 A6 43 SO 59 WA11 75 WD12 91 LDR1 107 MOD 123 TP4 / 12 D5 28 A5 44 VDD2 60 WA12 76 WD4 92 LDG5 108 REVC 124 /FIQ / 13 D4 29 A4 45 WA0 61 WA13 77 WD11 93 LDG4 109 GNDed 125 /RESET / 14 D3 30 A3 46 WA1 62 WA14 78 WD3 94 LDG3 110 GNDed 126 TP2 / 15 D2 31 A2 47 WA2 63 WA15 79 WD10 95 LDG2 111 GNDed 127 TP3 / 16 D1 32 A1 48 WA3 64 GND 80 WD2 96 LDG1 112 GNDed 128 GND